## Slide 1: 50.012 Networks Lecture 5: Reliable Data Transfer – Part I
2021 Term 6
Assoc. Prof. CHEN Binbin

## Slide 2: Learning Goal
Understand principles behind reliable data transfer
  Read textbook Section 3.4
Gentle reminder:
  Lab 1 due 28 Sep (Tue) 23:59
  Quiz 1: this Friday 1 Oct 9am
    Cover the topics from week 1 and 2
    True/false and MCQ
    25 minutes
    Open book, but no peer-to-peer discussion

## Slide 3: Principles of reliable data transfer
important in application, transport, link layers
  top-10 list of important networking topics!
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 4: Principles of reliable data transfer
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)
important in application, transport, link layers
  top-10 list of important networking topics!

## Slide 5: Principles of reliable data transfer
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)
important in application, transport, link layers
  top-10 list of important networking topics!

## Slide 6: Reliable data transfer: getting started
send
side
receive
side
rdt_send(): called from above, (e.g., by app.). Passed data to
deliver to receiver upper layer
udt_send(): called by rdt,
to transfer packet over
unreliable channel to receiver
rdt_rcv(): called when packet arrives on rcv-side of channel
deliver_data(): called by rdt to deliver data to upper

## Slide 7: Reliable data transfer: getting started
we’ll:
incrementally develop sender, receiver sides of reliable data transfer protocol (rdt)
consider only unidirectional data transfer
  but control info will flow on both directions!
use finite state machines (FSM) to specify sender, receiver
state
1
state
2
event causing state transition
actions taken on state transition
state: when in this “state” next state uniquely determined by next event
event
actions

## Slide 8: Reliable data transfer: roadmap
rdt | Assumptions about underlying channel | #State (sender/ receiver) | Mechanism
1.0 | perfectly reliable | 1 / 1 | 
2.0 | Data packet corrupted with bit errors | 2 / 1 | Checksum ACK/NAK
2.1 | Both data & ACK corrupted with bit errors | 4 / 2 | Seq. #
2.2 | Same as 2.1 | 4 / 2 | Remove NAK
3.0 | With both error and loss | 4 / 2 | Countdown timer

## Slide 9: rdt1.0: reliable transfer over a reliable channel
underlying channel perfectly reliable
  no bit errors
  no loss of packets
separate FSMs for sender, receiver:
  sender sends data into underlying channel
  receiver reads data from underlying channel
Wait for call from above
packet = make_pkt(data)
udt_send(packet)
rdt_send(data)
extract (packet,data)
deliver_data(data)
Wait for call from below
rdt_rcv(packet)
sender
receiver

## Slide 10: rdt2.0: channel with bit errors
underlying channel may flip bits in packet
  checksum to detect bit errors
the question: how to recover from errors:
  acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK
  negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors
  sender retransmits pkt on receipt of NAK
new mechanisms in rdt2.0 (beyond rdt1.0):
  error detection
  receiver feedback: control msgs (ACK,NAK) rcvr->sender
How do humans recover from “errors”
during conversation?

## Slide 11: rdt2.0: channel with bit errors
underlying channel may flip bits in packet
  checksum to detect bit errors
the question: how to recover from errors:
  acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK
  negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors
  sender retransmits pkt on receipt of NAK
new mechanisms in rdt2.0 (beyond rdt1.0):
  error detection
  feedback: control msgs (ACK,NAK) from receiver to sender

## Slide 12: rdt2.0: FSM specification
Wait for call from above
sndpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
sender
receiver
rdt_send(data)
L

## Slide 13: rdt2.0: operation with no errors
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L

## Slide 14: rdt2.0: error scenario
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L

## Slide 15: rdt2.0 has a fatal flaw!
What is that?

## Slide 16: rdt2.0 has a fatal flaw!
what happens if ACK/NAK corrupted?
sender doesn’t know what happened at receiver!
can’t just retransmit: possible duplicate
handling duplicates:
sender retransmits current pkt if ACK/NAK corrupted
sender adds sequence number to each pkt
receiver discards (doesn’t deliver up) duplicate pkt
stop and wait
sender sends one packet,
then waits for receiver
response

## Slide 17: rdt2.1: sender, handles garbled ACK/NAKs
Wait for call 0 from above
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
Wait for ACK or NAK 0
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isNAK(rcvpkt) )
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isNAK(rcvpkt) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
Wait for
call 1 from above
Wait for ACK or NAK 1
L
L

## Slide 18: rdt2.1: receiver, handles garbled ACK/NAKs
Wait for
0 from below
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq0(rcvpkt)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
Wait for
1 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq0(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq1(rcvpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)

## Slide 19: rdt2.1: discussion
sender:
seq # added to pkt
two seq. #’s (0,1) will suffice. Why?
must check if received ACK/NAK corrupted
twice as many states
  state must “remember” whether “expected” pkt should have seq # of 0 or 1
receiver:
must check if received packet is duplicate
  state indicates whether 0 or 1 is expected pkt seq #
note: receiver cannot know if its last ACK/NAK received OK at sender

## Slide 20: rdt2.2: a NAK-free protocol
same functionality as rdt2.1, using ACKs only
instead of NAK, receiver sends ACK for last pkt received OK
  receiver must explicitly include seq # of pkt being ACKed
duplicate ACK at sender results in same action as NAK: retransmit current pkt

## Slide 21: rdt2.2: sender, receiver fragments
Wait for call 0 from above
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
Wait for ACK
0
sender FSM
fragment
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK1, chksum)
udt_send(sndpkt)
Wait for
0 from below
rdt_rcv(rcvpkt) &&
(corrupt(rcvpkt) ||
has_seq1(rcvpkt))
udt_send(sndpkt)
receiver FSM
fragment
L

## Slide 22: rdt3.0: channels with errors and loss
new assumption: underlying channel can also lose packets (data, ACKs)
  checksum, seq. #, ACKs, retransmissions will be of help … but not enough
approach: sender waits “reasonable” amount of time for ACK
retransmits if no ACK received in this time
if pkt (or ACK) just delayed (not lost):
  retransmission will be duplicate, but seq. #’s already handles this
  receiver must specify seq # of pkt being ACKed
requires countdown timer

## Slide 23: rdt3.0 sender
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
Wait for ACK0
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
Wait for
call 1 from above
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,0) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,1)
stop_timer
stop_timer
udt_send(sndpkt)
start_timer
timeout
udt_send(sndpkt)
start_timer
timeout
rdt_rcv(rcvpkt)
Wait for
call 0from above
Wait for ACK1
L
rdt_rcv(rcvpkt)
L
L
L

## Slide 24: rdt3.0 in action
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
pkt1
ack1
ack0
ack0
(a) no loss
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(b) packet loss
pkt1
X
loss
pkt1
timeout
resend pkt1

## Slide 25: rdt3.0 in action
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(c) ACK loss
ack1
X
loss
pkt1
timeout
resend pkt1
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
send ack0
rcv ack0
send pkt1
send pkt0
rcv pkt0
pkt0
ack0
(d) premature timeout/ delayed ACK
pkt1
timeout
resend pkt1
ack1
send ack1
send pkt0
rcv ack1
pkt0
ack1
ack0
send pkt0
rcv ack1
pkt0
rcv pkt0
send ack0
ack0
rcv pkt0
send ack0
(detect duplicate)

## Slide 26: Performance of rdt3.0
rdt3.0 is correct, but performance stinks
e.g.: 1 Gbps link, 15 ms prop. delay, 8000-bit packet:
  U sender: utilization – fraction of time sender busy sending
  if RTT=30 msec, 1KB pkt every 30 msec: 33kB/sec thruput over 1 Gbps link
network protocol limits use of physical resources!
Dtrans =
L
R
8000 bits
109 bits/sec
=
=
8 microsecs

## Slide 27: rdt3.0: stop-and-wait operation
first packet bit transmitted, t = 0
sender
receiver
RTT
last packet bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R

## Slide 28: Reliable data transfer: summary
rdt | Assumptions about underlying channel | #State (sender/ receiver) | Mechanism
1.0 | perfectly reliable | 1 / 1 | 
2.0 | Data packet corrupted with bit errors | 2 / 1 | Checksum ACK/NAK
2.1 | Both data & ACK corrupted with bit errors | 4 / 2 | Seq. #
2.2 | Same as 2.1 | 4 / 2 | Remove NAK
3.0 | With both error and loss | 4 / 2 | Countdown timer